## Slide 1: Rail fixtures & fastening
All the fitting which is used for linking of rail end to end & also for fixing rails to the sleeper in track are known as fixture & fastening

## Slide 2: Rail fixtures & fastening

## Slide 3: Types of fixtures & fastening
Fish plate
Bearing plate
Chairs
Spikes
Bolts
Keys & cotters
Anchors & anticreepers

## Slide 4: Fish plate
Used to maintain the continuity of rail in a track
Made of mild steel 20mm thick 456cm long provided with 4no. Of 32mm dia. Hole at 114mm c/c

## Slide 5: Function of fish plate
To maintain continuity of rail in track
To allow expansion & contraction of rail due to temp.
To maintain correct alignment at each rail joint

## Slide 6: Bearing plate
The placed between flat footed rails & wooden sleeper
Type
Flat bearing plates
Canted bearing plate

## Slide 7
Flat bearing plates
Canted bearing plate

## Slide 8: Function of bearing plate
To prevent sinking of rail in wooden sleeper
To distribute the load uniformly
To enable the spike to be held tight
To prevent shifting of rail
To eliminate adding of wooden sleeper
To maintain gauge when bearing plate are used
To achieve economy

## Slide 9: Spike
It is require to fix the rail, bearing plates or chairs to woooden sleeper

## Slide 10: Requirement of good spike
They should be strong enough to hold the rail, bearing plate and chair in proper position
They should be easy in fixing and removing
They should not come out due to vibrations
They should be cheap

## Slide 11: types
Screw spike
Round spike
Standard spike
Dog spike
Screw spike
Round spike
Standard spike

## Slide 12: Elastic spike

## Slide 13: Bolt
To connect various joint in track

## Slide 14: Function
To connect fish plate to rail
To connect chair or bearing plate to timber sleeper
To connect sleeper to bridge girdeer

## Slide 15: Types
Fang bolt
Hook bolt
FISH BOLT

## Slide 16: keys
It is require to keep the rail in proper position

## Slide 17: Type
Timber keys
Metal key
Stewart key
Spring coiled key
Morgan key

## Slide 18: Anchor or Anti creeper
It is used to prevent the creep in rail
They are available in different shape
The no of anti creeper depend upon amount of creep occurring in the track