## Slide 1: PROCESS PLANNING

## Slide 2: PROCESS PLANNING
“ Determining the most appropriate manufacturing processes and the sequence in which they should be performed to produce a given part or product specified by designed Engineering”.
It can also be defined as “The systematic determination of the processes by which a product is to be manufactured economically & competitively”.

## Slide 3: PROCESS PLANNING
The system or a process responsible for the conversion of raw material in to finished product by the most economical way within the limit of design specifications.
The process parameters which is used to convert the part into the final product.
Process planning is the intermediate stage between DESIGNING & MANUFACTURING of the product.

## Slide 4: Defining Process Planning
In general, the inputs to Process Planning are:
Design data
Raw material data
Facilities data (machining data, tooling data, fixture data etc)
Quality requirements data
Production type data
The output of process planning is the process plan:
Process Plan Sheet
Process Sheet
Operation Sheet
Planning Sheet
Route Sheet
Route Plan
Part Program

## Slide 5: FUNCTIONS OF PROCESS PLANNING
Process Planning has the following important functions:
To determine the basic manufacturing process.
To determine the sequence of operations.
To determine the equipment's and tooling required.

## Slide 6: Who does Process Planning ?
Tradionally, Process Planning is done by manufacturing engineers who are familiar with the particular processes in the factory and are able to read engineering drawings.
Based on their Knowledge, skill and experience, they develop the processing steps in the most logical sequence required to make each part.
Some details are often delegated to specialists, such as tools designers.

## Slide 7: PROCESS PLANNING CONSITS OF
Jigs & fixtures
Material to be used
Specifying the inspection stages
Sequence of operations to be performed
Selecting the proper machines
Selecting the proper tools
Details like speed, feed, depth of cut, etc.

## Slide 8: INFORMATION REQUIRED FOR PP
The following information is needed to develop a process plan.
Knowledge of Various manufacturing processes.
Engineering drawing of the component.
Knowledge of various tooling and fixtures.
Relative costs of various processes, tooling and raw materials.
Resources available in the factory.
Ability to do computations on machining time and cost.
Knowledge to use reference books, such as machinability data handbook.

## Slide 9: PLANNING OF PROCESSES FROM RAW MATERIAL TO FINISHED PRODUCT
Part Print Analysis
Make or buy decision
To Select Basic Manufacturing Process
To Determine the Sequence of Operation
Combine the Operations
Selection of Machine Tools and Equipment
Inspection
Miscellaneous Functions
Preparation of Operation

## Slide 10: FACTORS AFFECTING PROCESS PLANNING
Production Methods
Size and Type of raw material
Process Capability
Quantity to be manufactured
Delivery dates of the products
Surface finish and accuracy required

## Slide 11: COMBINED OPERATIONS
The cost of processing can be reduced by eliminating unnecessary operations.
This can be achieved in number of ways and are accomplished through proper planning.
Operations can be performed in two ways:
By Simulation
By Integration

## Slide 12: By Simulation
Simulation involves those combinations where two or more elements of an operation, or two or more operations are performed at the same time.
Example: series of hole to be drilled simultaneously using a multiple spindle drill press. Cuter are specially designed.

## Slide 13: By Integration
Where several individual elements of an operation or group of operations are combined in succession but not simultaneously.
Example: Taping is done after drilling hole on the same set up by just changing the tool.

## Slide 14: ADVANTAGES OF COMBINED OPERATIONS
Improved accuracy
Reduced labor cost
Reduced plant fixed cost
Less tooling required
Less handling required
Fewer setups
Smaller in process inventory
Less scrap
Fewer inspection points required

## Slide 15: DISADVANTAGES OF COMBINED OPERATIONS
Maintaining tool accuracy
Possible higher tool costs
Maintaining dimensions for several baselines
More costly setups
 Sometimes scrap is increased
Compromises on operational speed
Chip disposal

## Slide 16: INSPECTION
Quality related in-process inspection is an essential part of quality control in manufacturing.
It includes measuring, examining or testing one or more characteristics of a product or process.
Inspection includes separation of defective parts from the non-defective parts.

## Slide 17: TYPES OF INSPECTION
FLOOR
Done at work station itself
CENTRALIZED
Special cell located in the industry

## Slide 18: DETERMINATION OF INSPECTION STAGES
Quality inspection serves three main purposes:
Identification of the problem.
Preventing its occurrence.
Elimination of the problem.
Type of production system.
Type of layout.
Type of machine used.

## Slide 19: PURPOSE OF INSPECTION
To distinguish good lots from bad lots.
To distinguish good pieces from bad pieces.
To determine if the process is changing.
To rate quality of product.
To rate accuracy of inspectors.
To measure precision of instruments.
To secure products design information.

## Slide 20: STAGES OF INSPECTION
Inspection of incoming material.
Inspection during the manufacturing process.
Inspection of Production processes.
Inspection of finished goods when it is completely manufactured.
Inspection of the product before delivery, if material is stored from long time.