## Slide 1: ROBOTICS

## Slide 2: Definition of Robot:
“A robot is a reprogrammable, multifunctional manipulator designed to move material, parts, tools or specialized devices through variable programmed motions for the performance of a variety of tasks”
Statement by : Robotics institute of America
OR
A mechanical device with joints and links, guided by sensors and driven by actuators, controlled by a programme,that handle and manipulate parts,material,tools and devices for performing different tasks in various work conditions…..

## Slide 3: LAWS OF ROBOTICS
Isaac Asimov proposed three “Laws of Robotics” and later added the “zeroth law”
• Law 0: A robot may not injur humanity or through inaction, allow humanity to come to harm
• Law 1: A robot may not injure a human being or through inaction, allow a human being to come to harm, unless this would violate a higher order law
• Law 2: A robot must obey orders given to it by human beings, except where such orders would conflict with a higher order law
• Law 3: A robot must protect its own existence as long as such protection does not conflict with a higher order law

## Slide 4: DEGREE OF FREEDOM
Each plane in which a robot can move.
Ability of the robot arm to move forward, backward, up down and to the left and right.
For each DOF, a joint is required
A robot requires 6 DOF to be completely versatile.

## Slide 5: 6 DOF
Rotational movement
Vertical movement
Radial movement
Pitch
Yaw
Roll

## Slide 6: 6 dof robot arm animation.mp4

## Slide 7: BASIC COMPONENTS OF ROBOT
1. Arm
2. End Effectors
3. Actuators
4. Sensors
5. Controllers
6. Drive
7. Software

## Slide 8: JOINTS AND LINKS
The manipulator of an industrial robot consists of a series of joints and links.
Each joint is connected to two links, an input link and an output link
A robotic link is the rigid component of the robot manipulator.

## Slide 9: TYPES OF MECHANICAL JOINTS

## Slide 10: ROBOT ANATOMY
The manipulator of an industrial robot consists of a series of joints and links.
Different joints and links comprise the study of robot anatomy,
Means assembling of outer components of a robot such as wrist, arm and body
Robotic manipulator consists of 2 sections:
Body and arm assembly (3 DOF)
Wrist assembly (3 DOF)

## Slide 11: BODY AND ARM CONFIGURATIONS

## Slide 13: ROBOT WRIST ASSEMBLY
The roll joint is accomplished by use of a T joint;
The pitch joint is achieved by recourse to an R joint; and
The yaw joint, a right-and-left motion, is gained by deploying a second R joint.

## Slide 14: END EFFECTORS:
An end effector is usually attached to the robot’s wrist, and it allows the robot to accomplish a specific task.
This means that end effectors are generally custom-engineered and fabricated for each different operation.
The two general categories of end effectors are grippers and tools.

## Slide 15: GRIPPERS
Grippers grasp and manipulate objects during the work cycle.
Typically the objects grasped are work parts that need to be loaded or unloaded from one station to another.

## Slide 16: Magnetised gripper
Vacuum gripper
Mechanical gripper

## Slide 18: TOOLS
Tools are used to perform processing operations on the work part.
Typically the robot uses the tool relative to a stationary or slowly-moving object
For example, spot welding, arc welding, and spray painting—which all use a tool for processing the operation—may all be carried-out in this way.

## Slide 19: GRIPPER AND TOOL (SPOT WELDING)

## Slide 20: ACTUATORS
Actuators convert the energy into mechanical form
Classification:
Hydraulic actuators
Pneumatic actuators
Electrical actuators

## Slide 21: ELECTRICAL ACTUATORS
Converts electrical signal commands into mechanical motions.
Commonly used are servo motor and stepper motor
DC MOTORS
AC MOTORS
STEPPER MOTOR

## Slide 22: HYDRAULIC/PNEUMATIC ACTUATORS
LINEAR – converts hydraulic energy into linear motion
ROTARY – converts hydraulic energy into rotary motion
ACTUATORS TO OPERATE FLOW CONTROL VALVES – used to control the flow and pressure of fluids such as gases, steam or liquid

## Slide 23: SENSORS
SENSORS
CONTACTING
NON CONTACTING
TOUCH SENSORS
FORCE SENSORS
OPTICAL SENSORS
PROXIMITY SENSORS
MACHINE VISION
MISCELLANOUS TYPE

## Slide 24: ADVANCED SENSOR TECHNOLOGIES IN ROBOTICS

## Slide 25: CONTROL SYSTEM
Joint movements must be controlled if the robot is to perform as desired.

## Slide 26: ROBOT PROGRAMMING
A robot program is a path in space to be followed by the manipulator, combined with peripheral actions that support the work cycle.
To programme a robot, specific commands are entered into the robot’s controller memory, and this action may be performed in a number of ways.

## Slide 27: PROGRAMMING METHODS
Lead through programming -work cycle is taught to robot by moving the manipulator through the required motion cycle and simultaneously entering the program into controller memory for later playback
Robot programming languages -uses textual programming language to enter commands into robot controller
Simulation and off-line programming –program is prepared at a remote computer terminal and downloaded to robot controller for execution without need for leadthrough methods

## Slide 28: INDUSTRIAL ROBOT APPLICATIONS
Material handling
Processing operations
Assembly and inspection.

## Slide 29: MATERIAL HANDLING APPLICATIONS

## Slide 30: PROCESSING OPERATIONS

## Slide 31: ASSEMBLY AND INSPECTION
In assembly and inspection robots can be used for material handling applications, and for processing applications, so it is in effect a hybrid of the previous two application categories.
Owing to difficulties in both assembly and inspection, the application of robots to these tasks has been found to be somewhat difficult.