## Slide 1: CHAPTER-05 FRANCIS TURBINE SUB: FLUIDS MECHANICS & MACHINERY Prepared By: Ms.Nilesha U.Patil

## Slide 2
Program : Mechanical Engineering Course: Fluid Mechanics & Machinery CO-Select various types of turbine under specified condition.

## Slide 3: Introduction
A turbine is a rotary mechanical device that extracts energy from a fluid flow and converts it into useful work.
Turbines are used in boat propulsion systems, hydroelectric power generators, and jet aircraft engines.

## Slide 4: Basic Types of Turbine
Steam Turbine
Water Turbine
Wind Turbine

## Slide 5: Types Based Energy Used
Impulse turbine : Only kinetic energy of water is used to drive turbine.
Eg.Pelton Turbine
Reaction turbine : Kinetic energy as well as Pressure energy of water is used to drive turbine.
Eg.Francis Turbine

## Slide 6: Introduction
Francis turbines are the most common water turbine in use today.
They operate in a water head from 10 to 650 meters (33 to 2,133 feet).
They are primarily used for electrical power production.
The turbine powered generator power output generally ranges from 10 to 750 megawatts

## Slide 7: Sir James B. France
This turbine was invented by Sir James B. France in Lowell, Massachusetts, U.S.A.
Studying the Boyden turbine ,Francis was able to redesign it to increase efficiency.
Boyden Turbine could achieve a 65 percent efficiency.
So, James France redesigned this turbine and new turbine with 88% efficiency was invented.
This was known as ‘Francis turbine’.

## Slide 8: The Boyden Turbine

## Slide 9: Francis Turbine
It is an inward flow reaction turbine of mixed flow type , in which ,water enters the runner radially at its outer peripheri and leaves axially at its centre.

## Slide 10: The Francis Runner
X blade runner
Traditional runner

## Slide 11: The Francis Turbine

## Slide 12: Working
Penstock: It is a large size conduit which conveys water from the upstream to the dam/reservoir to the turbine runner.
Spiral Casing: It constitutes a closed passage whose cross-sectional area gradually decreases along the flow direction; area is maximum at inlet and nearly zero at exit.
Guide Vanes: These vanes direct the water on to the runner at an angle appropriate to the design, the motion of them is given by means of hand wheel or by a governor.
Governing Mechanism: It changes the position of the guide blades/vanes to affect a variation in water flow rate, when the load conditions on the turbine change.
Runner and Runner Blades: The driving force on the runner is both due to impulse and reaction effect. The number of runner blades usually varies between 16 to 24.
Draft Tube: It is gradually expanding tube which discharges water, passing through the runner to the tail race.
Hydraulic efficiency varies between 85-90%.

## Slide 13: Francis Turbine Power Plant : A Continuous Hydraulic System

## Slide 14: Parts of A Francis Turbine

## Slide 15
Water from spiral casing
Water particle

## Slide 16
Runner inlet (Φ 0.870m)
Guide vane outlet for designα) (Φ 0.913m)
Closed
Position
Max. Opening Position

## Slide 17: Operation of Guide Vanes
.

## Slide 18
Hydraulic efficiency of Francis Hydraulic System

## Slide 19: Advantages
It is a most widely used turbine in world (about 70-80%).
Effective use of water pressure as well as velocity.
It is American standard turbine.
Very good efficiency(80-94%).

## Slide 20: Disadvantages
Cost is High.
Due to its complex design and large number of moving parts, maintenance and repair is difficult and costly.
It is applicable to flow of medium head only.

## Slide 21: Recent Advancements:
New types of designs are developed to reduce cost and complexity of mechanism.
Modified turbine include Inline Linkless Francis Turbine, Cross-flow Turbine,etc.
These new turbine require less space, simplified designs, less moving parts, etc.

## Slide 22: Thank You